## Slide 1: Giromill type

## Slide 2: General data about VAWTS
The main advantage of a vertical axis wind turbine, however, is that it turns in any direction with the wind; so, they do not need the yaw mechanism that is required in the horizontal axis design.
As a result, the use of the vertical axis wind turbine may be efficient; although of having some disadvantages such as, they cannot cover a large area of wind. They are not very efficient with regards to extraction of energy because they operate near the ground where the air flow is turbulent.

## Slide 3: ABOUT GIROMILL

## Slide 4
An example of the design of Giromill wind turbine was previously carried out and the analysis of some design parameters was explained by Solum et al ,The designed wind turbine was a three bladed 12 kW H-rotor with tapered NACA 0018 wing sections. It is connected to the rotating shaft through airfoiled struts with a Cp of about 0.35. Also, the experimental results for this turbine were introduced and studied by Deglaire et al,the turbine performance was investigated in highly turbulent wind conditions and it was found that it is reacting fairly well with respect to these conditions.

## Slide 6: VAWT design parameters
The wind turbine parameters considered in the design process are:
1. Turbine swept area
2. Number of blades
3. Tip speed ratio
4. Turbine Aspect ratio
5. Turbine solidity
6. Mass moment of inertia
7. Pitch angle
8. Airfoil type

## Slide 7: 1-Turbine swept area
The swept area is the section of air that encloses the turbine in its movement, the shape of the swept area depends on the rotor configuration, this way the swept area of an HAWT is circular shaped while for a straight-bladed vertical axis wind turbine the swept area has a rectangular shape and is calculated using: 𝐴=2𝑅𝐻

## Slide 8: 2-Number of blades
The number of blades has a direct effect in the smoothness of rotor operation as they can compensate cycled aerodynamic loads. For even number of blades as two blades the fluctuation in rotor torque was higher than odd number of blades as three blades turbine. Such behavior could represent a great advantage for three-bladed small VAWT architectures, for which the increased manufacturer and installation costs are not as important as for large rotors

## Slide 9: 3-Tip speed ratio
The tip speed ratio is an extremely important factor in wind turbine design, which is defined as the ratio of the tangential speed at the blade tip to the actual wind speed, 𝑇𝑆𝑅=𝜔𝑅/𝑢∞ Where R is the radius of the hub, and ω is the angular speed of blades.
If the blade angular speed ω is too small, most of the wind may pass undisturbed though the blade swept area making little useful work on the blades. On the contrary, if ω is too large, the fast rotating blades may block the wind flow reducing the power extraction. Each rotor design has an optimal tip speed ratio at which the maximum power extraction is achieved

## Slide 10: 4-Turbine aspect ratio
The ratio between blade height to rotor radius (aspect ratio) is play an important role in design process of VAWT, Basically high aspect ratio means that we get high rotational speed than rotor torque for the same power and vice versa. Aspect ratio influences the Reynolds number and as a consequence the power coefficient

## Slide 11: 5-Turbine solidity
The solidity σ is defined as the ratio between the total blade area and the projected turbine area ,It is an important non-dimensional parameter which affects self-starting capabilities and for straight bladed VAWTs is calculated with: 𝜎=𝐵∗𝑐/𝑅
Where B is the number of blades, c is the blade chord; it is considered that each blade sweeps the area twice. This formula is not applicable for HAWT as they have different shape of swept area.
Solidity determines when the assumptions of the momentum models are applicable, and only when using high σ ≥ 0.4 a self-starting turbine is achieved

## Slide 12: 6-Mass moment of inertia
The biggish moment of inertia is disadvantage of VAWT’s start, effecting reasonable design ( rate of high and radius )and result of brake Therefore , it is necessary that study the influence of moment of inertia of VAWT.
Angular acceleration = Aerodynamic moment / Mass moment of inertia
The VAWT of the lesser moment of inertia has good start performance, but the steady of performance is bad with wind velocity increased; it’s because that the process is unsteady when wind turbine is rotated, that is to say, the angular velocity is different at the different azimuth angle, the angular velocity has obvious wave with azimuth angle’s difference for the lesser moment of inertia’s wind turbine

## Slide 13: 7-Pitch angle
It was clearly seen that proper airfoil selection make great contributions to the improvement of aerodynamic performance, but it was difficult to give consideration to self-staring capability, higher power coefficient and wider operational region. Fortunately, it was found out that pitch angle had significant impacts on overall performance of wind turbine

## Slide 14: 8-Airfoil type
Airfoil proper selection for your VAWT is important in many ways. The airfoil should be selected based on many factors:
1. Chambered or symmetrical
2. Lift/drag ratio
3. Aerodynamic performance to increase output power
4. Airfoil thickness

## Slide 20: Effect of number of blades on Cp, Ct and TSR
As shown in Figs. 10–13, these curves were obtained from changing the number of blades (2, 3 and 4 blades) with different variations of pitch angles, turbine radii, chord lengths and airfoil types.
We can see from Figs. 10 and 12 that using four blades results in the highest performance regarding Cp, Ct and TSR
(Cp =25% at TSR= 1.3 and Ct= 0.205 at TSR =1) and when decreasing the number of blades to two blades the performance was much decreased. It can be seen from Figs. 11 and 13 that when decreasing the number of blades to three blades there is a small decrease in performance. So, we can conclude that increase in the number of blades from two to four blades has a significant effect in increasing the performance while increasing the number of blades from three to four has a small increase in performance. This is expected as the higher number of blades results in higher torque at the same speed.

## Slide 21: Effect of turbine radius on Cp, Ct and TSR
As shown in Figs. 14 and 15, these curves were obtained from changing the turbine radius (20 cm and 40 cm) with different variations of number of blades, pitch angles, chord lengths and airfoil types.
We can see from Figs. 14 and 15 that; when we decrease the turbine radius from 40 cm to 20 cm, the performance was much decreased showing the significant effect of changing the turbine radius.The lower performance at the lower radius is due to the effect of the shaft and the downwind blades on the flow past the blades which decrease the velocity of the wind past the upwind blades.

## Slide 22: Effect of airfoil type on Cp, Ct and TSR
As shown in Figs. 16–19, these curves were obtained from changing the airfoil type (NACA 0024, NACA 4420 and NACA 4520) with different variations of number of blades,turbine radii, chord lengths and pitch angles.
As shown in Figs. 16 and 18, the symmetrical airfoil NACA 0024 results in higher performance regarding Cp, Ct and TSR; the airfoil NACA 0024 gives higher Cp compared to NACA 4420 and NACA 4520. There is a significant improvement in performance results from using NACA 0024 airfoil instead of NACA 4520, while there is a much lower improvement in performance results from using NACA 4420 airfoil instead of NACA 4520.

## Slide 23: Effect of chord length on Cp, Ct and TSR
As shown in Figs. 20–23, these curves were obtained from changing the chord length (8 cm, 12 cm and 15 cm) with different variations of number of blades, turbine radii, pitch angles and airfoil types. Figs. 20 and 22 show that increasing the chord length has a significant effect in increasing performance, while Figs. 21 and 23 give the same conclusion but at different pitch angle.
This can be explained due to the higher projected area which increases the aerodynamic force on the blades and due to the higher Re number which results in higher Cl values with increasing the chord length.

## Slide 24: SOME DATA AFTER TESTING IN WIND TUNNEL

## Slide 26: BIBLIOGRAPHY
Abramovic. (1987). Vertical Axis wind turbines: asurvey and bibliography. Wind engineering, 334-343.
Alaimo. (2015). 3D CFD analysis of a vertical axis wind turbine. energies, 3013-3033.
Allet. (1997). On the aerodynamic modelling of VAWT. Wind Engineering, 351-365.
Battisti. (2012). Gli impianti motori eolici. Battisti Editore.
Battisti, L. (2016). Analysis of different blade architechtures on small VAWT performance. Journal of physics conference series.
Biadgo. (2013). Numerical and analytical investigation of vertical axis wind turbine. FME Transaction, 49-58.

## Slide 27: CONTINUE
Brown. (2010). Design and Analysis of A vertical axis thermoplastic composite wind turbine blade. Plastics, Rubber and Composites, 111-121.
Brusca. (2014). Design of a vertical axis wind turbine: how the aspect ratio affect the turbine's performance. international journal Energy environment engineering , 333-340.
Burton. (2001). Wind energy handbook. Sussex: John Wiley & Sons.
Carrigan. (2012). Aerodynamic shape optimization of a vertical axis wind turbine using differential evolution. ISRN renewable energy, 16.
Castelli. (2013). Numerical Evaluation of the Contribution of internal and Aerodynamic Forces on VAWT blade loading. Aerospace and mechanical engineering.

## Slide 28: CONTINUE
Castelli, M. (2011). The Darrieus wind turbine: Proposal for a new performance prediction model. Energy, 4919-4934.
Castillo. (2011). Small-scale vertical axis wind turbine design. Tamper university of applied scince .
Chang. (2005, october). Advanced topics in environmental engineering - wind power. Retrieved from University of New Brunswick: http://www.ece.unb.ca/powereng/courses/EE6693/index.html
Claessens. (2006). The design and testing of airfoils for applications in small vertical axis wind turbines. Delft: Delft university of technology faculty of aerospace engineering.
Darrieus. (1931). Turbine having its rotating shaft transverse to the flow of the current. Us patent.

## Slide 29: CONTINUE
Duncan. (1962). An elementary treatise on the mechanics of fluids. Edward Arnold Ltd.
Edwards. (2008). Wind tunnel and numerical study of a small vertical axis wind turbine. 46th AIAA Aerospace Scinces Meeting and exhibit. Nevada.
El.Ali, M. (2007). Comparison between solar and wind energy in lebanon. 9th international conference on electrical power quality and utilisation. Barcelona.
Ferreira. ( 2007). Simulating dynamic stall in a 2D VAWT:modeling strategy, verification and validation with particle image velocimetry data. Journal of physics, Vol. 75.
Golding. (1976). The generation of electricity by wind power. New York: John Wiley.
Gorlov. (1998). Development of the helical reaction hydraulic turbine. US department of energy

## Slide 30: CONTINUE
Gupta. (2010). Computational fluid dynamics analysis of a twisted three bladed H-Darrieus rotor. Journal of Renewable and sustainable energy.
Hill. (2009). Darrieus turbines: the physics of self starting. jpurnal ofpower and energy, 21-29.
Islam. (2008). Aerodynamic models for Darrieus type straight bladed vertical axis wind turbines. Renewable and Sustainable Energy Reviews, 1087-1109.
Islam, M. (2008). Design analysis of fixed-pitch straight bladed vertical axis wind turbines with an alternative material. Windsor: Mechanical, Automotive and materials engineering department, University of windsor, Canada.
King. (2004). Farmers of forty centuries: Organic Farming in China, Korea and Japan. Courier Publications.
Klimas. (1981). Effects of blade preset Pitch/offeset on curved-blade Darrieus vertical axis wind turbine performance . Sandia National Laboratories.

## Slide 31: CONTINUE
Lanzafame. (2014). 2D CFD modeling of H-Darrieus wind turbines using a transittion turbulance model. Energy procedia, 131-140.
Lazauskas. (1992). Three pitch control systems for vertical axis wind turbines compared. Wind Engineering, 269-282.
Marten. (2013). QBlade: An open source tool for design and simulation of horizontal and vertical axis wind turbines. International journal of emerging technology and advanced engineering, 264-269.
(2005). MECH 4010 Design Project Vertical Axis Wind Turbine. Dalhousie: Department of Mechanical Engineering Dalhousie university.
Muller. (2009). Vertical axis resistance type wind turbines for use in buldings. Renewable energy, 34.
Mulugeta. (2015). Numerical and analytical investigation of vertical axis wind turbine. Belgrade: Faculty of mechanical engineering .

## Slide 32: CONTINUE
Paraschivoiu. (2002). Wind turbine design. 148.
Premkumar. (2015). Numerical studies on the effect of cambered airfoil blades on self starting of vertical axis wind turbine part1: NACA 0012 and NACA 4415. Applied mechanics and material, 250-254.
Quang. (2014). Flow-driven rotor simulation of vertical axis tidal turbines: A comparison of helical and straight blades. International journal of naval architecture and ocean engineering, 257-268.
Sabaeifard. (2012). Determinatin of vertical axis wind turbines optimal configuration through CFD simulations. International conferance of future environment and energy OPCBEE vol.28.
Sathyajith. (2006). Wind energy fundamentals, resource analysis and economics. springer.

## Slide 33: CONTINUE
Schaffarczyk. (2014). Introduction to wind turbine aerodynamics. Springer, 1-12.
Shepherd. (1994). Historical development of windmill . wind turbine technology: Fundamental concepts of wind turbine Engineering ASME, 1-46.
Strickland. (1975). The darrieus turbine: a performance prediction model using Multiplestream tubes. Albuquerque: Sandia National Laboratories.
Strickland. (1986). A review of aerodynamics analysis methods for vertical axis wind turbines. 5th ASME wind energy symposium, (pp. 7-17). New Orleans, USA.
Templin. (1974). Aerodynamic performance theory for the NRC vertical axis wind turbine. Ottawa: National research council.
Tong, W. (2010). Wind Power Generation and Wind turbine design. WIT Press.

## Slide 34: CONTINUE
Torresi. (2008). Accurate numerical simulation of high solidity wells turbine. Renewable energy, 735-747.
Touryan. (1987). Electric power from vertical axis wind turbines. Propulsion and Power, 481-493.
Tullis. (2008). medium-solidity vertical axis wind turbines.
Vaishnav. (2007). An investigation on the aerodynamic performance of A vertical axis wind turbine. Durg: Bhilai institute of technology.
Vallverdu. (2014). Study on vertical axis wind turbine using streamtube and dynamic stall models. Chicago: Illinois institute of technology.
Vassberg. (2005). Revisiting the vertical axis wind turbine design using advanced computational fluid dynamics. 43rd AIAA Aerospace scinces meeting and exhibit, (pp. 12783-12805). Nevada .

## Slide 35: CONTINUE
Wang. (2011). 6-DOF numerical simulation of the vertical axis water turbine. Joint fluids Engineering conference. Shizuoka.
Wilson. (1994). Aerodynamic behavior of wind turbines. wind turbine technology: Fundamental concepts of wind turbine engineering, 215-282.
Wind Atlas. (2005). Retrieved from New and renewable energy authority: http://www.nrea.gov.eg/Ar/Technology/Windatlas
Windfinder. (2018, July 6). Wind statics-Alexandria Airport/Nouzha. Retrieved from Windfinder
Yang. (2013). Effect of moment of inertia to H type vertical axis wind turbine aerodynamic performance. 6th international conference on pumps and fans with compressors and wind turbines. Lanzhou: School of energy and power engineering, University of technology, Lanzhou, China.
Zhang. (2014). effect of blade pitch angle on aerodynamic performance of straight-bladed vertical axis wind turbine. Journal of centeral south university press and springer, 1417-1427.